## Slide 1: Warm Up: Measurement and Measurement Error
 Record all certain digits in a measurement plus last estimated or uncertain digit
 The stated uncertainty should match the
measurement precision
 E.g. A length of 10.5 cm ± 0.2 cm
A mass of 26.7 g ± 0.1 g
A temperature of 24.5 C ± ______ ?
Why is this not a good way to record a length?
21 cm ± 0.2 cm
Answer:
0.1 C
There is a mismatch in precision between the recorded value and error!

## Slide 2: New Concept: Absolute and Relative Errors & Error Propagation
Absolute error is expressed in the units as the measurement
E.g. 16.5 cm ± 0.2 cm
1.265 kg ± 0.005 kg
Relative or Percent error is expressed as a percentage of the given measurement
E.g. 3.8 kg ± 2.0 %
5.6 m ± 5.0 %

## Slide 3: Converting between Absolute and Relative Uncertainty
Convert to relative uncertainty:
8.4 kg ± 0.5 kg
Convert to absolute uncertainty:
12.6 m ± 4%
Answer: 8.4 kg ± 6%
Answer: 12.6 ± .5 m

## Slide 4: Propagating Errors
When adding or subtracting numbers we ADD the absolute uncertainties
When multiplying or dividing numbers we ADD the relative uncertainties
Find the absolute uncertainty when these lengths are added:
(1.5 m ± 0.2 m) + (1.36 m ± 0.05 m) + (2.85 m ± 0.08 m)
=
5.71 m ± 0.33 m  5.7 ± 0.3 m
Find the relative uncertainty when lengths are multiplied to find volume:
(1.5 m ± 0.1 m) x (1.36 m ± 0.05 m) x (2.85 m ± 0.05 m)
=
5.814 m3 ± (6.67% +3.67% + 1.75%)
 5.814 m3 ± 12.1%  5.8 ± 0.7 m3